## Slide 1
Topic 14
Timing Issues

## Slide 2: Outline
Timing requirements for FSM
Setup time and hold time
Asynchronous input and metastability
Synchronizer
Switch debouncing
Clock skew
Hazards

## Slide 3: State Machine
Finite State Machine
Combinational
Logic
Inputs
State
Register
Present
State (PS)
Outputs
Feedback of
present state
Next State
(NS)
FSM Outputs

## Slide 4: Clocking Methodology for FSM
Combinational logic transforms data during clock cycles
  Between clock edges
Clock cycles should be
  Long enough to allow combinational logic completes computation
    Longest delay determines clock period
  Short enough to ensure acceptable performance and to capture small changes on external inputs

## Slide 5: Hardware Constraints – Setup and Hold
An edge-triggered flip-flop will not operate correctly if the data is not stable for a sufficient time before and after the clock edge
Storage element may be put in nondeterministic state
Setup Time
  Minimum time that data must be stable prior to the triggering edge
Setup-time violations are cause by combinational paths that are long relative to the clock cycle
  Fix: stretch clock, optimize combinational circuit, split combinational circuit, pipelining,
Setup Time
Clock

## Slide 6: Hardware Constraints – Setup and Hold
Hold Time:
  Minimum time that data must remain stable after the triggering edge
Hold-time violations are caused by short paths that allow a signal to propagate from a source flip-flop to a destination flip-flop and change the data that was created in the previous cycle before the destination flip-flop has registered its output
  Fix: insert buffers, use different flip flop
Setup and hold time: ns
Hold interval
Clock

## Slide 7: Metastability and Asynchronous Inputs
If the setup or hold time of an edge-triggered flip-flop is violated the flip-flop may enter a metastable state.
  Metastable state: Any flip-flop state other than stable 1 or 0
    Eventually settles to one or other, but we don’t know which
  For internal circuits, we can make sure setup time is satisfied
  But what if input comes from external (asynchronous) source, e.g., button press?
State_0
State_1
State_m
Metastable state

## Slide 8: Metastable State
Assuming D = 0  1 while rising edge of clock (0  1)
  May oscillate and never stops if D and clock changes at exactly same time
  In reality, DFF will settle eventually after some time (hopefully within a clock cycle)
D
Q
Q’
Clock
D
Clock
P4
P3
P1
P2
5
6
1
2
3
Q’
Q
4

## Slide 9: Asynchronous Inputs
In a fully synchronous system, all circuits are driven by a common clock, and the state registers may change only under the control of the clock
  Synchronous system may be driven by asynchronous inputs which may put flip flops into the metastable state
Examples: Keyboard activity, push buttons, and interrupts to a computer.
Problems caused by asynchronous inputs
  The unpredictable arrival of an asynchronous input may cause a setup condition to be violated.
  Glitches on the asynchronous inputs may cause system failure.
  Asynchronous fanout path delays might cause some input transitions to be "caught " by some devices and "missed" by others.
General rule: Ensure that all inputs are synchronous, i.e. synchronize them to the clock signal. Reset and set can be exceptions.

## Slide 10: Synchronizer
Use a D-type flip flop to synchronize the input.
Asynchronous
Input
Synchronous
system
D
Clk
Q
clock
Synchronizer
Synchronized input

## Slide 11: Synchronizer Failure
The systems input is synchronized, but the setup and hold conditions of the synchronizing flip-flop may be violated.
  The synchronizing flip-flop may enter a metastable state and disrupt system operation.
The flip-flop may be in metastable state, then its state will be nondeterministic, its output may be interpreted as
  “0”, or
  “1”, or
  enter a metastable state, output is not synchronized anymore
A circuit that uses the output of a synchronizer that is in the metastable state is said to experience a synchronizer failure.
To recover from a synchronizer failure
  wait for the circuit to leave the metastable state, the time is unpredictable, or
  execute a reset to put the system into a known state.

## Slide 12: Double DFF Synchronizer
Reduce the possibility of synchronizer failure
  Use flip-flops having the shortest possible setup and hold intervals
  stretch the clock period to allow more time for the circuit to recover
    Output final settles in 0 or 1
    But means slower circuit
  Insert double-synchronizing D-type flip-flops after the asynchronous inputs
Inputs
Synchronous
system
D
Clk
Q
D
Clk
Q
clock
FF_1
FF_2

## Slide 13: Double DFF Synchronizer
Both flip-flop must enter a metastable state to have a synchronizer failure
The first flip-flop might enter a metastable state, but has a clock period to recover
It is less likely that FF_2 will see an input that is not valid, thus it is less likely that FF_2 will enter a metastable state
  Typically, 1 clock cycle is long enough for 1st DFF to recover
  Output of 2nd DFF is synchronized and stable, but unpredictable
Asynchronous
Input
Synchronous
system
D
Clk
Q
D
Clk
Q
clock
Synchronizer
Synchronized input
FF_1
FF_2

## Slide 14: Synchronizer with More FFs
More FFs is unnecessary
However, synchronizer failure can never be 100% avoided
  We can just maximize the Mean Time Between Failures (MTBF) -- a number often given along with a circuit
ai
synchronizers
l
o
w
very
low
very
very
low
incredibly
l
o
w

## Slide 15: Bouncing Switch
Asynchronous input to a synchronous logic circuit may be created by a mechanical switch or a push button (mechanical component)
When changing from one position to another, the switch may bounce away from the contact point
Data
V
DD
Data
Data
analog
Digitized version

## Slide 16: Switch Debouncing
Debouncing circuit: SR latch
When throw is at position 0,
S = 1, R = 0, Data = 0
When throw changes to position 1
R = 1, S = (0 1), Data = 1
Data is latched regardless of S
assuming switch won’t bounce
back to position 0 and touch it
Data
S
R
V
DD
r1
V
DD
r2
0
1
S R Q Q+ 0 0 0 X 0 0 1 X 0 1 0 1 0 1 1 1 1 0 0 0 1 0 1 0 1 1 0 0 1 1 1 1
not allowed
set
reset
hold

## Slide 17: Switch Debouncing
D Flip Flop may be used
for switch debouncing
But clock needs careful design
D
Clock_L
Data_L
Clock_S
Data_S

## Slide 18: Switch Debouncing
The clock signal triggering the D flip flop should be slow enough to allow the switch to settle
The clock should be fast enough to allow the asynchronous input to take effect as soon as possible
Bouncing time: ms
The D flip flop may be replaced by
a double DFF synchronizer
  thus both synchronizing and
  debouncing will be taken care of
  by one circuit

## Slide 19: Clock Skew
Example: add synchronous control to a D flip flop
  Choice 1: control the input by mux
  Choice 2: gated clock
Gated clock is not a good practice
  Flip flops that have gated clock will observe the clock change later than flip flops that have direct clock;
  The situation in which the clock signal arrives at different flip flops at different times is known as clock skew
Clock skew may cause
synchronous circuit behaves
asynchronously
D
Q
Q
Data
Clock
Ld
D
Q
Q
Q
Data
Clock
Ld
0
1

## Slide 20: Clock Skew
Clock skew should be minimized as much as possible
  H-Tree: carefully designed distribution network try to create the same length from each flip flop to the clock source
  If same length may not be achieved, buffers are inserted on the short paths to even the delay
Same for the global asynchronous reset

## Slide 21: Glitches and Static Hazards
The output of a combinational circuit may make a transition even
though the patterns applied at its inputs do not imply a change.
These unwanted transitions are called glitches.
A circuit in which a glitch may occur is said to have a hazard.
static 1-hazard
static 0-hazard
0-Hazard
1-Hazard

## Slide 22: Static Hazards
Static hazards are caused by different propagation delays on the
reconvergent fanout paths
Example: F = AC + BC'
Initial inputs: A = 1, B = 1, C = 1 and F = 1
New inputs: A = 1, B = 1, C = 0 and F = 1
With non-zero propagation delays, the path to F1 will be longer than the path to F0, causing a change in C to reach F1 later than it reaches F0.

## Slide 23: Static Hazards Example

## Slide 24: Static Hazards
00
10
11
01
0
1
0
AB
C
0
1
1
1
0
1
0
Redundant
cube
00
10
11
01
0
1
0
AB
C
0
1
1
1
0
1
0
F = AC + BC'
Hazards might not be significant in a
synchronous sequential circuit if the
clock period can be stretched
A hazard is problematic in an
asynchronous circuit (including Mealy FSM)
If transition is within the same group
in the K-map, hazard won’t occur
  will occur when transition from one
  group to another
Hazard Removal
A static hazard can be removed by
using a redundant PI
F = AC + BC’ + AB

## Slide 25: Static Hazards Example
Static 1-Hazard-Free circuit

## Slide 26: Static Hazards
Static 0 hazard might not be removed in a static 1 hazard free circuit
To eliminate static 0 hazard:
  method 1: cover the adjacent 0s in the corresponding POS expression
  method 2: first eliminate the static 1 hazards. Then verify in the K-map if 0 hazards have been eliminated already
Eliminating static 1 hazard
F = a'c' + bc + a'b
00
10
11
01
00
01
11
10
1
ab
cd
1
0
0
1
1
1
0
0
1
1
0
0
0
0
1
m0
m1
m3
m2
m4
m5
m7
m6
m12
m13
m15
m14
m8
m9
m11
m10
Cover by
adding a'b to
eliminate
static-1 hazard
a'c'
bc
Eliminating static 0 hazard
F = (a' + c) (b + c') (a' + b)
= a'c' + bc + a'b
11
10
00
10
11
01
00
01
1
ab
cd
1
0
0
1
1
1
0
0
1
1
0
0
0
0
1
m0
m1
m3
m2
m4
m5
m7
m6
m12
m13
m15
m14
m8
m9
m11
m10
Cover by
adding (a + b')
to eliminate
static-0 hazard

## Slide 27: Dynamic Hazards
Dynamic Hazard: output changes more than once as a result of a single output change
Dynamic hazards are a consequence of multiple static hazards caused by multiple reconvergent paths in a multi-level circuit.
Hazard Removal:
  Elimination of all static hazards eliminates dynamic hazards.
Dynamic Hazard

## Slide 28: Dynamic Hazards Example
F_static has a static hazard
F_dynamic has a dynamic hazard
A
C
B
F_static
F_dynamic
First
reconvergence
Second
reconvergence
F0
F1
C_late

## Slide 29: Dynamic Hazards Example
00
10
11
01
0
1
0
AB
C
0
1
1
1
0
1
0
Redundant group
Eliminates both
1-hazard and
0-hazard

## Slide 30: Functional Hazard
Solutions to both static hazard and dynamic hazard are based on the assumption that only one input is changing at a time
When more than one input changes occur at the same time, the hazard caused is more complicated to remove
Example:
0  1
1  0
0  1
1  0
1  0  1
1  0  0
0  0  1

## Slide 31: Functional Hazard
Simulation with delay
Simulation without delay. Many sim tools show this to warn for functional hazard

## Slide 32: Functional Hazard
Functional hazards are unsolvable hazards which occur when more than one input variable changes at the same time
Hazards such as functional hazards can not be logically eliminated as the problem lies with actual specification of the circuit
K-map view of the functional hazard
 | 0 | 1
0 | 0 | 1
1 | 1 | 0
A
B